## Slide 1: Unit 6: Safe Loading and Transportation of Children Using Adaptive Equipment

## Slide 2: Attention to detail, patience, caring
Willingness to ask questions

## Slide 3: Lift Use and 5 Mistakes to Avoid
Distraction while operating lift
Drivers or aides riding the lift with the child
Children riding lift standing up
Dangling jewelry, clothing, long hair, which could be caught in the lift machinery
Allowing children or untrained adults to operate lift

## Slide 4: Wheelchair Securement
The Challenge
  Securement systems can be complicated
      Wheelchairs come in a wide variety of designs, sizes, weights
      Finding suitable securement points can be difficult
      Even a small securement mistake can result in a WC tipping over
      Many children have been injured in such incidents
Securement Tips
  Attach straps to main WC frame near welded joints
  Never attach to removable or folding components or wheels
  45 degree angle
  Lap/shoulder passenger restraints must be used
  Sensitivity when fastening belts
  Children can help
  Shake-Test before the bus moves
  Check securement during ride

## Slide 5: Safety Seats
Manufacturer’s instructions must be followed carefully
Adequately tightening safety seats in school buses can be difficult but is essential
Use 2 people to secure a safety seat, one kneels on the safety seat, one tightens the belt
Secure seats before picking up children

## Slide 6: TLC Driving
Vulnerable passengers deserve special driving skills
Children lacking upper body strength and control, or with brittle bone syndrome, can be seriously injured if the bus hits a bump too hard
Bumps are magnified in the rear of the bus, catapult effect
Smooth starts, stops and turns are the sign of a professional driver
Rushing erodes defensive driving skills

## Slide 7: Unit 6 Review
Why does loading and transportation of children in wheelchairs require attention to detail, patience, caring and the willingness to ask questions?
Describe procedures for safe lift use.
Describe procedures for safely securing a wheelchair in a bus.
Describe how to secure a safety seat into a bus seat.
What is TLC driving and why is important when transporting children in wheelchairs?